## Slide 1: Assembly Programming Language
CSE2214 - Flow Control Instructions
Chapter – 6 (Charles Marut, Ytha Yu)
Prepared By-
Asma Enayet, Lecturer, CSE, DU

## Slide 2: Conditional Jumps -Signed Jumps

## Slide 3: -Unsigned Jump

## Slide 4: -Single-Flag Jumps

## Slide 5: Example of Jump
MOV CX, 256
MOV DL, 0
MOV AH, 2
PRINT_LOOP:
INT 21H
INC DL
DEC CX
JNZ PRINT_LOOP
Also an example of a simple loop !

## Slide 6: Conditional Jumps
JNZ destination_label
Range 126 bytes ! How do you overcome that?
Introduce another unconditional jump !

## Slide 7: The CMP Instruction
CMP destination, source
CMP AX,BX ; (AX-BX) sets flags result wise
JG BELOW

## Slide 8: Signed Versus Unsigned Jumps
If AX = 7FFFh (0111111111111111),
BX = 8001h (1000000000000001)
CMP AX,BX
JG BELOW ; Interprets in Signed Manner
CMP AX,BX
JA BELOW ; Interprets in Unsigned Manner

## Slide 9: Working with Characters
- In working with the standard ASCII character set, either signed or unsigned jumps may be used, because the sign bit of a byte containing a character code is always zero. However, unsigned jumps should be used when comparing extended ASCII chars (code 80h to FFh).

## Slide 10: What happens here?
MOV CX, AX
CMP BX, CX
JLE NEXT
MOV CX, BX
NEXT :
Bigger value is initiated in CX !

## Slide 11: The JMP Instruction
-JMP destination
-JMP can be used to get around the range restriction of a conditional jump. For example, suppose we want to implement the following loop:
TOP:
;body of the loop
DEC CX
JNZ TOP
MOV AX,BX ; next instruction
and the loop body contains so many instructions that label TOP is out of range for JNZ (more than 126 bytes before JMP TOP). We can do this:
TOP :
; body of the loop
DEC CX ; decrement counter
JNZ BOTTOM ; keep looping if ex > 0
JMP EXIT
BOTTOM :
JMP TOP
EXIT :
MOV AX,BX ; next instruction

## Slide 12: Branching Structures -IF-THEN
IF condition is TRUE
THEN
execute true-branch statements
END_IF
IF AX < 0
THEN
replace AX by -AX
END_IF
CMP AX, 0
JNL END_IFF
NEG AX
END_IFF :

## Slide 13: IF-THEN-ELSE
IF condition is true
THEN
execute true-branch statements
ELSE
execute false-branch statements
END_IF
IF AL <= BL
THEN
display the character in AL
ELSE
display the character in BL
END_IF
MOV AH, 2
CMP AL,BL
JNBE ELSE_
MOV DL,AL
JMP DISPLAY
ELSE_ :
MOV DL,BL
DISPLAY :
INT 21h

## Slide 14: SWITCH-CASE
CASE expression
Values_1: statements_1
values_2: statemeents_2
.
.
.
values_n: statements_n
END_CASE
CASE AX
<0: put -1 in BX
=0: put o in BX
>0: put l in BX
END_CASE
CMP AX,0
JL NEGATIVE
JE ZERO
JG POSITIVE
NEGATIVE:
MOV BX, -1
JMP END_CASE
ZERO:
MOV BX, 0
JMP END_CASE
POSITIVE:
MOV BX, 1
END_CASE:
MOV AH, 4Ch
INT 21H

## Slide 15: Branches with Compound Conditions -AND Conditions
Read a character (into AL)
IF ('A' => character) and
(character <= 'Z')
THEN
display character
END IF
; read a character
MOV AH, 1
INT 21H
CMP AL, 'A'
JNGE END_IF
CMP AL, 'Z'
JNLE END_IF
MOV DL, AL
MOV AH, 2
INT 21H
END_IF :
; YOUR CODE IF CONDITIONS DIDNT MEET

## Slide 16: Branches with Compound Conditions -AND Conditions
DIY
CLASS ASSIGNMENT COMING UP !

## Slide 17: Looping Structure -FOR LOOP
The LOOP instruction can be used to implement a FOR loop. It has the form
LOOP destination_label
The counter for the loop is the register CX which is initialized to loop_count.
Execution of the LOOP Instruction causes CX to be decremented automatically.
if CX is not 0, control transfers to destination_label. If CX==0, the next instruction after LOOP is done. destinatlon_label must precede the LOOP instruction by no more than 126 bytes.

## Slide 18
MOV CX, 80d
MOV AH, 2
MOV DL, '*'
TOP:
INT 21h
LOOP TOP
MOV AH, 4Ch ; WHEN CX==0, THIS LINE GETS THE CONTROL AUTOMATICALLY
INT 21H
; Prints * 80 times !
Continued…

## Slide 19: Continued…
If CX contains 0 when the loop is entered, the LOOP instruction causes CX to be decremented to FFFFh.
The loop is then executed FFFFh = 65535 more times! To prevent this, the instruction JCXZ (jump if CX is zero) MAY BE used before the loop.
JCXZ destination_label
JCXZ SKIP
TOP:
;body of the loop
LOOP TOP
SKIP:

## Slide 20: -WHILE LOOP
; counting number of chars in a line
MOV DX,0 ; DX counts characters
MOV AH,1 ; prepare to read
INT 21H
WHILE_:
CMP AL, 0DH ; CR?
JE END_WHILE ; yes, exit
INC DX ; not CR, increment count
INT 21H ; read a character
JMP WHIILE_
END_WHILE:
MOV AH, 4CH
INT 21H
Lets See an example of it !

## Slide 21: -REPEAT LOOP
REPEAT
statements
UNTIL condition
; executes at least once, Do While loop !
MOV AH, 1
REPEAT: INT 21H
CMP AL,'A'
JNE REPEAT ; keeps reading until an A is found as input

## Slide 22: WHILE Versus REPEAP
In many situations where a conditional loop is needed, use of a WHILE loop or a REPEAT loop is a matter of personal preference.
Advantage of a WHILE is that the loop can be bypassed if the terminating condition is initially false, whereas the statements in a REPEAT must be done at least once.
Code for a REPEAT loop is likely to be a little shorter because there is only a conditional jump at the end, but a WHILE loop has two jumps, a conditional JMP at the top and a JMP at the bottom.

## Slide 23: Thanks !
Any questions ??
“NO”
OKAY LETS GET TO THE BUSINESS NOW, LETS SOLVE A PROBLEM !!


## Slide 24
ODD : Using proper prompts and indentation, take any integer value as input. If the number is either less than
4 or greater than 6, output “OUT OF RANGE !”.
Otherwise Output “IN RANGE !”
EVEN : Using proper prompts and indentation, take any capital letter character as input. If the character is A or E or I or O or U, output “VOWEL !”. Otherwise Output “CONSONANT !”
30 minutes, starts from right now. Turn off the monitor power button when time-end is declared.